Final Exam Study Guide

Homework Questions and Answers:
Homework 1 Questions and Answers:
1)
How long does it take a packet of length 1, 000 bytes to propagate over a link of distance 2, 500 km, propagation speed 2.5 ∗ 10^8 m/s, and transmission rate 2 Mbps? More generally, how long does it take a packet of length L to propagate over a link of distance d, propagation speeds, and transmission rate R bps? Does this delay depend on packet length? Does this delay depend on transmission rate?

2,500,000 meters / 270 meters/second = 9259 seconds

If, however, it’s actually supposed to be 2.5 * 10^8, the answer would be .01 seconds.

Propagation delay does not depend on packet length, nor does it depend on transmission rate.

*This question is actually, for our class’s purposes, referring to transmission delay, which is N/R, where N is the number of bits and R is the transmission rate.

2)
What is the difference between a virus and a worm?

A virus is a self-replecating infection by receiving/executing object. A worm, however, is a passively receiving object that gets itself executed. In other words, worms do not need human action (such as the downloading of an email attachment) to propagate.

3)
Review the car-caravan analogy in Section 1.4. Assume a propagation speed of 100 km/hour. (a) Suppose the caravan travels 150 km, beginning in front of one tollbooth, passing through a second tollbooth, and finishing just after a third tollbooth. What is the end-to-end delay? (b) Repeat (a), now assuming that there are eight cars in the caravan instead of ten.

Propagation delay = distance/speed = 150 km/100km/h = 90 minutes.
Transmission delay = 12/60 seconds * 10 cars = 2 minutes.

a. 90 mins + 2 mins * 3 toll booths = 96 mins.
b. 90 mins + (12/60 * 8)*3 = 94.8 mins.

4)
Suppose two hosts, A and B, are separated by 20, 000 kilometers and are connected by a direct link of R = 2 Mbps. Suppose the propagation speed over the link is 2.5 ∗ 108 meters/sec. (a) Calculate the bandwidth-delay product, R ∗ dprop. (b) Consider sending a file of 800, 000 bits from Host A to Host B. Suppose the file is sent continuously as one large message. What is the maximum number of bits that will be in the link at any given time? (c) Provide an interpretation of the bandwidth-delay product. (d) What is the width (in meters) of a bit in the link? Is it longer than a football field? (e) Derive a general expression for the width of a bit in terms of the propagation speed s, the transmission rate R, and the length of the link m.

a. 20,000,000 meters/2.5*10^8 meters/second (I’m assuming the 2.5 * 108 was a typo, because that value doesn’t make any sense) * 2000000 bits = 160,000 bits
b. 160,000 bits.
c. Bandwidth delay product is how much data can be on the line at once (or rather at any given time).

Homework 2 Questions and Answers:
Suppose you wanted to do a transaction from a remote client to a server as fast as possible. Would you use UDP or TCP? Why?

UDP has fewer RTTs. With TCP you have to make a connection with the server for requests and replies.

Describe how Web caching can reduce the delay in receiving a requested object. Will Web caching reduce the delay for all objects requested by a user or for only some of the objects? Why?

Frequently visited websites store data, such as images, that may have high overhead, in a local cache. Web caching does not reduce the delay for all objects, as not all accessed objects are cached locally.

Consider an e-commerce site that wants to keep a purchase record for each of its customers. Describe how this can be done with cookies.

The user has a unique cookie number that stores data about them. This e-commerce site would have this user’s cookie ID number tied to a function that returns their shopping history whenever they visit this site.

From a users perspective, what is the difference between the downloadanddelete mode and the download-and-keep mode in POP3?

Download and delete erases your messages from your server once you collect them. For mobile users who want access to their emails and attachments, the download-and-keep method allows them to get those emails from other computers or devices, downloading the same emails multiple times across multiple machines.

Consider an HTTP client that wants to retrieve a Web document at a given URL. The IP address of the HTTP server is initially unknown. What transport and application-layer protocols besides HTTP are needed in this scenario?

Transport and application-layer protocols beyond HTTP? So, the methods in HTTP that are requesting data is HTTP’s GET method. In order to get the IP address of the server it wants to talk to, it needs to initiate a DNS request (which runs on UDP). After it gets the IP address, it initiates a TCP connection with the server. So, overall UDP and TCP for DNS and HTTP respectively.

Consider a short, 10-meter link, over which a sender can transmit at a rate of 150 bits/sec in both directions. Suppose that packets containing data are 100,000 bits long, and packets containing only control (e.g., ACK or handshaking) are 200 bits long. Assume that N parallel connections each get 1/N of the link bandwidth. Now consider the HTTP protocol, and suppose that each downloaded object is 100 Kbits long, and that the initial downloaded object contains 10 referenced objects from the same sender. (a) Would parallel downloads via parallel instances of non-persistent HTTP make sense in this case? (b) Now consider persistent HTTP. Do you expect significant gains over the non-persistent case?

The time for parallel downloads will be approximately 7400 + (8*One way propagation delay) seconds.
This is found by the time it takes to receive the first object, (3*250/150) + 100000/150, plus the time it takes to receive the remaining objects now that bandwidth has been split amongst the objects, (3*200/15) + 100000/15 seconds (not considering propagation delay).

Similarly, the time for persistent HTTP will also be approximately 7300 + (24*Propagation delay) seconds. This can be shown as (3*250/150) + 100000/150 + (200/150 + 10*100000/150) seconds for the base (ie non-propagation delay transport time). If propagation delay for these ten objects is 10/300*10^6, then each instance of propagation delay has a virtually negligible impact on the speed of either method.

So, a) yes, as it is not significantly different to persistent HTTP, and b) there are no real benefits between either method given this example.

Consider distributing a file of F = 15 Gbits to N peers. The server has an upload rate of us = 30 Mbps, and each peer has a download rate of di = 2,(∀i ∈ {1, 2, ..., N}) Mbps and an upload rate of u. For N = 10, 100, and 1, 000 and u = 300 Kbps, 700 Kbps, and 2 Mbps, prepare a chart giving the minimum distribution time for each of the combinations of N and u for both: (a) client-server distribution and (b) P2P distribution.

Minimum distribution time is the maximum of {NF/us OR F/dmin} for client server. For P2P it is maximum of {F/us, F/di, NF/(us+∑ui)}.

Homework 3 Questions and Answers:

(a) Consider a TCP connection between Host A and Host B. Suppose that the TCP segments traveling from Host A to Host B have source port number x and destination port number y. What are the source and destination port numbers for the segments traveling from Host B to Host A? (b) Describe why an application developer might choose to run an application over UDP rather than TCP.

a. The source port number will be Y and the destination port number should be X.

b. Some people might have an application that sends data that can tolerate some loss, such as video streaming or audio streaming. Also some developers might not want to have to deal with TCP congestion control protocols.

In the Reliable Data Transfer (rdt) protocols, (a) why did we need to introduce sequence numbers? (b) why did we need to introduce timers?

a. Sequence numbers are important for receivers to know whether it’s receiving a new packet or a duplicate of an already received packet.

b. Timers are important for detecting loss. If an ack message is not received within a particular window then the sender can assume a loss has been incurred, allowing it to resend the needed packets.

UDP and TCP use 1s complement for their checksums. Suppose you have the following three 8-bit bytes: 01010011, 01100110, 01110100. What is the 1s complement of the sum of these 8-bit bytes? (Note that although UDP and TCP use 16-bit words in computing the checksum, for this problem you are being asked to consider 8-bit sums.) Show all work. Why is it that UDP takes the 1s complement of the sum; that is, why not just use the sum? With the 1s complement scheme, how does the receiver detect errors? Is it possible that a 1-bit error will go undetected? How about a 2-bit error?

   1 11 - > carries
   01010011
+ 01100110

   1 11
= 10111001
+ 01110100
= 00101101
→ 1’s Complement = 11010010

1’s complement makes it easier to detect errors. The receiver knows there’s been an error if the sum contains a 0. All 1 bit errors are detected, but 2 bit errors can still go undetected.

Host A and B are communicating over a TCP connection, and Host B has already received from A all bytes up through byte 126. Suppose Host A then sends two segments to Host B back-to-back. The first and second segments contain 80 and 40 bytes of data, respectively. In the first segment, the sequence number is 127, the source port number is 302, and the destination port number is 80. Host B sends an acknowledgment whenever it receives a segment from Host A. (a) In the second segment sent from Host A to B, what are the sequence number, source port number, and destination port number? 1 (b) If the first segment arrives before the second segment, in the acknowledgment of the first arriving segment, what is the acknowledgment number, the source port number, and the destination port number? (c) If the second segment arrives before the first segment, in the acknowledgment of the first arriving segment, what is the acknowledgment number? (d) Suppose the two segments sent by A arrive in order at B. The first acknowledgment is lost and the second acknowledgment arrives after the first timeout interval. Draw a timing diagram, showing these segments and all other segments and acknowledgments sent. (Assume there is no additional packet loss.) For each segment in your figure, provide the sequence number and the number of bytes of data; for each acknowledgment that you add, provide the acknowledgment number.

a.
Sequence number: 207
Source port number: 302
Destination port number: 80

b.
Acknowledgement number: 207
Source port number: 80
Destination port number: 302

c.
Acknowledgement number: 127

d.

Host A is sending an enormous file to Host B over a TCP connection. Over this connection there is never any packet loss and the timers never expire. Denote the transmission rate of the link connecting Host A to the Internet by R bps. Suppose that the process in Host A is capable of sending data into its TCP socket at a rate S bps, where S = 10 R. Further suppose that the TCP receive buffer is large enough to hold the entire file, and the send buffer can hold only one percent of the file. Elaborate: (a) What would prevent the process in Host A from continuously passing data to its TCP socket at rate S bps? (b) TCP flow control? (c) TCP congestion control? (d) Or something else?

a. This question is simply prefacing the following 3 questions, so it doesn’t really require elaboration.

b. Since the buffer can hold the entire file, there is no danger in being sent too much data at once.

c. There is also no packet loss and acknowledgements get sent before the timer expires, so there is no need for congestion control.

d. The sender simply can’t send much of the data at once because it’s buffer will fill up too quickly.

Homework 4 Questions and Answers:

We noted that network layer functionality can be broadly divided into data plane functionality and control plane functionality. (a) What are the main functions of the data plane? (b) What are the main functions of the control plane?

The data plane refers to the part of a router that controls/decides what to do with incoming packets, such as forwarding them to specific client devices. The forwarding table is managed in the data plane and the control plane helps or serves the functions of the data plane. The control plane executes routing protocols, handles the routing table, and other management functions.

Suppose that an arriving packet matches two or more entries in the forwarding table of a router. With traditional destination-based forwarding, what rule does a router apply to determine which of these rules should be applied to determine the output port to which the arriving packet should be switched?

Longest prefix match rule.

(a) Do routers have IP addresses? If so, how many? (b) When a large datagram is fragmented into multiple smaller datagrams, where are these smaller datagrams reassembled into a single larger datagram? (c) What is the 32-bit binary equivalent of the IP address 223.1.3.27?

a. Routers have 2 IP addresses. One for each of its interfaces.

b. Datagrams are reassembled at destination.

c. 11011111.00000001.00000011.00011011

Consider the network as shown in Figure 1. (a) Show the forwarding table in router A, such that all traffic destined to host H3 is forwarded through interface 3. (b) Can you write down a forwarding table in router A, such that all traffic from H1 destined to host H3 is forwarded through interface 3, while all traffic from H2 destined to host H3 is forwarded through interface 4?

a.
Destination Address	Link Interface
H3	3

b. No, forwarding rules are based solely on destination address.

Consider a datagram network using 32-bit host addresses as in Figure 2. Suppose a router has four links, numbered 0 through 3, and packets are to be forwarded to the link interfaces as follows: (a) Provide a forwarding table that has five entries, uses longest prefix matching, and forwards packets to the correct link interfaces (b) Describe how your forwarding table determines the appropriate link interface for datagrams with destination addresses: i. 11001000 10010001 01010001 01010101 ii. 11100001 01000000 11000011 00111100 iii. 11100001 10000000 00010001 01110111

a.

Prefix	Link Interface
11100000	0
11100001 01000000	1
11100000 1	2
11100001	3
OTHERWISE	0

b.
1) Interface 3 (OTHERWISE)
2) Interface 1
3) Interface 3

Consider a subnet with prefix 128.119.40.128/26. Give an example of one IP address (of form xxx.xxx.xxx.xxx) that can be assigned to this network. Suppose an ISP owns the block of addresses of the form 128.119.40.64/26. Suppose it wants to create four subnets from this block, with each block having the same number of IP addresses. What are the prefixes (of form a.b.c.d/x) for the four subnets?

a.128.119.40.171
b.128.119.40.64/28, 128.119.40.80/28, 128.119.40.96/28, 128.119.40.112/28

Consider the network setup in Figure 3. Suppose that the ISP instead assigns the router the address 24.34.112.235 and that the network address of the home network is 192.168.1/24. (a) Assign addresses to all interfaces in the home network. (b) Suppose each host has two ongoing TCP connections, all to port 80 at host 128.119.40.86. Provide the six corresponding entries in the NAT translation table.

a. Home addresses: 192.168.1.1, 192.168.1.2, 192.168.1.3. Router interface is 192.168.1.4.

b.
WAN Side	LAN Side
24.34.112.235, 5000	192.168.1.1, 3345
24.34.112.235, 5001	192.168.1.1, 3346
24.34.112.235, 5002	192.168.1.2, 3445
24.34.112.235, 5003	192.168.1.2, 3446
24.34.112.235, 5004	192.168.1.3, 3545
24.34.112.235, 5005	192.168.1.3, 3546